CS/EE 3810: Computer Organization
Lecture 15: Caching hierarchy
Anton Burtsev
November, 2022

---
Cache Hierarchies
Data and instructions are stored on DRAM chips – DRAM
   is a technology that has high bit density, but relatively poor
   latency – an access to data in memory can take as many
   as 300 cycles today!
Hence, some data is stored on the processor in a structure
   called the cache – caches employ SRAM technology, which
   is faster, but has lower bit density
Internet browsers also cache web pages – same concept

---
Memory Hierarchy
As you go further, capacity and latency increase
Disk
1 TB
10M cycles
Memory
16GB
300 cycles
L2 cache
2MB
15 cycles
L1 data or
instruction
Cache
32KB
2 cycles
Registers
1KB
1 cycle

---
Locality
Why do caches work?
Temporal locality: if you used some data recently, you
   will likely use it again
Spatial locality: if you used some data recently, you
   will likely access its neighbors
No hierarchy: average access time for data = 300 cycles
32KB 1-cycle L1 cache that has a hit rate of 95%:
        average access time = 0.95 x 1 + 0.05 x (301)
        = 16 cycles

---
Thank you!