CS/ECE 3810: Computer Organization
Lecture 4: MIPS instruction set
Anton Burtsev
August, 2022

---
Instruction Set
Understanding the language of the hardware is key to understanding
   the hardware/software interface
A program (in say, C) is compiled into an executable that is composed
   of machine instructions – this executable must also run on future
   machines – for example, each Intel processor reads in the same x86
   instructions, but each processor handles instructions differently
Java programs are converted into portable bytecode that is converted
   into machine instructions during execution (just-in-time compilation)
What are important design principles when defining the instruction
   set architecture (ISA)?

---
Instruction Set
Important design principles when defining the
   instruction set architecture (ISA):
keep the hardware simple – the chip must only
   implement basic primitives and run fast
keep the instructions regular – simplifies the
   decoding/scheduling of instructions
We will later discuss RISC vs CISC

---
A Basic MIPS Instruction
C code: a = b + c ;
Assembly code: (human-friendly machine instructions)
        add a, b, c # a is the sum of b and c
Machine code: (hardware-friendly machine instructions)
        00000010001100100100000000100000
Translate the following C code into assembly code:
        a = b + c + d + e;

---
Example
        C code a = b + c + d + e;
translates into the following assembly code:
        add a, b, c add a, b, c
        add a, a, d or add f, d, e
        add a, a, e add a, a, f
Instructions are simple: fixed number of operands (unlike C)
A single line of C code is converted into multiple lines of
   assembly code
Some sequences are better than others… the second
   sequence needs one more (temporary) variable f

---
Subtract Example
        C code f = (g + h) – (i + j);
Assembly code translation with only add and sub instructions:

---
Subtract Example
        C code f = (g + h) – (i + j);
translates into the following assembly code:
        add t0, g, h add f, g, h
        add t1, i, j or sub f, f, i
        sub f, t0, t1 sub f, f, j
Each version may produce a different result because
   floating-point operations are not necessarily
   associative and commutative… more on this later

---
Operands
In C, each “variable” is a location in memory
In hardware, each memory access is expensive – if
   variable a is accessed repeatedly, it helps to bring the
   variable into an on-chip scratchpad and operate on the
   scratchpad (registers)
To simplify the instructions, we require that each
    instruction (add, sub) only operate on registers
Note: the number of operands (variables) in a C program is
   very large; the number of operands in assembly is fixed…
   there can be only so many scratchpad registers

---
Registers
The MIPS ISA has 32 registers (x86 has 8 registers) –
    Why not more? Why not less?
Each register is 32 bits wide (modern 64-bit architectures
   have 64-bit wide registers)
A 32-bit entity (4 bytes) is referred to as a word
To make the code more readable, registers are
   partitioned as $s0-$s7 (C/Java variables), $t0-$t9
   (temporary variables)…

---
Binary Stuff
8 bits = 1 Byte, also written as 8b = 1B
1 word = 32 bits = 4B
1KB = 1024 B = 210 B
1MB = 1024 x 1024 B = 220 B
1GB = 1024 x 1024 x 1024 B = 230 B
A 32-bit memory address refers to a number between
   0 and 232 – 1, i.e., it identifies a byte in a 4GB memory

---
Memory Operands
Values must be fetched from memory before (add and sub)
   instructions can operate on them
 Load word
 lw $t0, memory-address
 Store word
 sw $t0, memory-address
How is memory-address determined?
Memory
Register
Memory
Register

---
Memory Address
The compiler organizes data in memory… it knows the
    location of every variable (saved in a table)… it can fill
    in the appropriate mem-address for load-store instructions
        int a, b, c, d[10]
…
Memory
Base address

---
Memory Organization
 $gp points to area in memory that saves global variables
Stack
Dynamic data (heap)
Static data (globals)
 $gp
Text (instructions)

---
Memory Instruction Format
The format of a load instruction:
        destination register
        source address
        lw $t0, 8($t3)
  any register
        a constant that is added to the register in parentheses

---
Memory Instruction Format
The format of a store instruction:
        source register
        destination address
        sw $t0, 8($t3)
  any register
        a constant that is added to the register in parentheses

---
Example
   int a, b, c, d[10];
   addi $gp, $zero, 1000 # assume that data is stored at
        # base address 1000; placed in $gp;
        # $zero is a register that always
        # equals zero
   lw $s1, 0($gp) # brings value of a into register $s1
   lw $s2, 4($gp) # brings value of b into register $s2
   lw $s3, 8($gp) # brings value of c into register $s3
   lw $s4, 12($gp) # brings value of d[0] into register $s4
   lw $s5, 16($gp) # brings value of d[1] into register $s5

---
Example
Convert to assembly:
C code: d[3] = d[2] + a;

---
Example
Convert to assembly:
C code: d[3] = d[2] + a;
Assembly (same assumptions as previous example):
        lw $s0, 0($gp) # a is brought into $s0
        lw $s1, 20($gp) # d[2] is brought into $s1
        add $s2, $s0, $s1 # the sum is in $s2
        sw $s2, 24($gp) # $s2 is stored into d[3]
Assembly version of the code continues to expand!

---
Memory Organization
The space allocated on stack by a procedure is termed the activation
   record (includes saved values and data local to the procedure) – frame
   pointer points to the start of the record and stack pointer points to the
   end – variable addresses are specified relative to $fp as $sp may
   change during the execution of the procedure
$gp points to area in memory that saves global variables
Dynamically allocated storage (with malloc()) is placed on the heap
Stack
Dynamic data (heap)
Static data (globals)
Text (instructions)

---
Binary Representation
The binary number
        01011000 00010101 00101110 11100111
       represents the quantity
       0 x 231 + 1 x 230 + 0 x 229 + … + 1 x 20
A 32-bit word can represent 232 numbers between
   0 and 232-1
     … this is known as the unsigned representation as
      we’re assuming that numbers are always positive
Least significant bit
Most significant bit

---
Negative Numbers
  32 bits can only represent 232 numbers – if we wish to also represent
  negative numbers, we can represent 231 positive numbers (incl zero)
  and 231 negative numbers
     0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
     0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
        …
     0111 1111 1111 1111 1111 1111 1111 1111two = 231-1
     1000 0000 0000 0000 0000 0000 0000 0000two = -231
     1000 0000 0000 0000 0000 0000 0000 0001two = -(231 – 1)
     1000 0000 0000 0000 0000 0000 0000 0010two = -(231 – 2)
        …
     1111 1111 1111 1111 1111 1111 1111 1110two = -2
     1111 1111 1111 1111 1111 1111 1111 1111two = -1

---
2’s Complement
     0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
     0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
        …
     0111 1111 1111 1111 1111 1111 1111 1111two = 231-1
     1000 0000 0000 0000 0000 0000 0000 0000two = -231
     1000 0000 0000 0000 0000 0000 0000 0001two = -(231 – 1)
     1000 0000 0000 0000 0000 0000 0000 0010two = -(231 – 2)
        …
     1111 1111 1111 1111 1111 1111 1111 1110two = -2
     1111 1111 1111 1111 1111 1111 1111 1111two = -1
Why is this representation favorable?
Consider the sum of 1 and -2 …. we get -1
Consider the sum of 2 and -1 …. we get +1
This format can directly undergo addition without any conversions!
Each number represents the quantity
   x31 -231 + x30 230 + x29 229 + … + x1 21 + x0 20

---
2’s Complement
     0000 0000 0000 0000 0000 0000 0000 0000two = 0ten
     0000 0000 0000 0000 0000 0000 0000 0001two = 1ten
        …
     0111 1111 1111 1111 1111 1111 1111 1111two = 231-1
     1000 0000 0000 0000 0000 0000 0000 0000two = -231
     1000 0000 0000 0000 0000 0000 0000 0001two = -(231 – 1)
     1000 0000 0000 0000 0000 0000 0000 0010two = -(231 – 2)
        …
     1111 1111 1111 1111 1111 1111 1111 1110two = -2
     1111 1111 1111 1111 1111 1111 1111 1111two = -1
Note that the sum of a number x and its inverted representation x’ always
equals a string of 1s (-1).
      x + x’ = -1
     x’ + 1 = -x … hence, can compute the negative of a number by
     -x = x’ + 1 inverting all bits and adding 1
Similarly, the sum of x and –x gives us all zeroes, with a carry of 1
In reality, x + (-x) = 2n … hence the name 2’s complement

---
Example
Compute the 32-bit 2’s complement representations
    for the following decimal numbers:
       5, -5, -6

---
Example
Compute the 32-bit 2’s complement representations
    for the following decimal numbers:
       5, -5, -6
     5: 0000 0000 0000 0000 0000 0000 0000 0101
    -5: 1111 1111 1111 1111 1111 1111 1111 1011
    -6: 1111 1111 1111 1111 1111 1111 1111 1010
   Given -5, verify that negating and adding 1 yields the
   number 5

---
Signed / Unsigned
The hardware recognizes two formats:
   unsigned (corresponding to the C declaration unsigned int)
   -- all numbers are positive, a 1 in the most significant bit
      just means it is a really large number
   signed (C declaration is signed int or just int)
   -- numbers can be +/- , a 1 in the MSB means the number
       is negative
This distinction enables us to represent twice as many
numbers when we’re sure that we don’t need negatives

---
MIPS Instructions
Consider a comparison instruction:
     slt $t0, $t1, $zero
and $t1 contains the 32-bit number 1111 01…01
What gets stored in $t0?

---
MIPS Instructions
Consider a comparison instruction:
     slt $t0, $t1, $zero
and $t1 contains the 32-bit number 1111 01…01
What gets stored in $t0?
The result depends on whether $t1 is a signed or unsigned
 number – the compiler/programmer must track this and
 accordingly use either slt or sltu
   slt $t0, $t1, $zero stores 1 in $t0
   sltu $t0, $t1, $zero stores 0 in $t0

---
Sign Extension
Occasionally, 16-bit signed numbers must be converted
   into 32-bit signed numbers – for example, when doing an
   add with an immediate operand
The conversion is simple: take the most significant bit and
   use it to fill up the additional bits on the left – known as
   sign extension
        So 210 goes from 0000 0000 0000 0010 to
       0000 0000 0000 0000 0000 0000 0000 0010
        and -210 goes from 1111 1111 1111 1110 to
       1111 1111 1111 1111 1111 1111 1111 1110

---
Alternative Representations
The following two (intuitive) representations were discarded
    because they required additional conversion steps before
    arithmetic could be performed on the numbers
sign-and-magnitude: the most significant bit represents
   +/- and the remaining bits express the magnitude
one’s complement: -x is represented by inverting all
   the bits of x
Both representations above suffer from two zeroes